## Slide 1: MADINAS Use Cases
S. Ringland (BT)
Rajat Ghai (Comcast)
M. Boucadair (Orange)

## Slide 2: Access Control based on MAC Addresses
CPEs widely support filtering features based MAC addresses
  An additional guard for access control such as accept- or discard-lists
Sample services:
  ISPs use MAC address filter to mitigate DDoS at the L2 edge. Filtering based on the IP address at the network side is suboptimal
  Schedule when a device can be granted access (e.g., parental control)
  Seek a confirmation from an administrator when a new device is detected

## Slide 3: Sticky DHCP Assignment for Incoming Connections
CPEs provide DHCP server service
It is quite common that users rely upon a sticky DHCP assignment to assign a static IPv4 address to a given device for various functions:
  DMZ
  (Static) Port Forwarding

## Slide 4: Local Diagnostic
ISPs need to be able to provide remote support for their customers to help identify and diagnose problems that the customers are having with their connectivity
Local diagnostic are executed by the CPE upon approval of the customer
  There is a need to be able to identify the current performance and behaviour of each individual device and to understand the patterns of performance of each device over a period of time that extends to at least several weeks
  Thus, there is a need for a persistent device identifier. For most diagnostics purposes the identifier only needs to be unique and persistent within an individual home network
ISPs also need to be able to discuss the performance of specific identified devices with the customer and so need to be able to tie the diagnostic device identifier to a device name or description that the customer will understand
  This is displayed locally by the CPE

## Slide 5: Usability: Community Wi-Fi Auto Sign-in
Many ISPs offer an open and secure SSID as a public Wi-Fi service to their customers across millions of APs
Many users access public Wi-Fi service using the open SSID
  First time authentication of a user is done via username/password provided by the supplicant
  Once the identity of the user is confirmed and verified the network caches the MAC address of the supplicant for provide auto auth to return users, until cache expiry.

## Slide 6: QoE Measurement & Improvement
Some Community Wi-Fi providers do continuous measurement of Quality Of Experience (QoE) of their users on the Wi-Fi network by scoring the QoE
Correlation of QoE experiments pre/post network tuning relies upon a persistent device identifier (MAC). For example:
  Device MAC “A” had a QoE score of “X”
  Operations team tunes that segment of the network, soak changes
  After Y days, QoE measurements are performed for device MAC “A” , and QoE score of “Z” is observed

## Slide 7: Legacy Client Steering and Pre-Association Steering
While the new Multi-band Operations based client steering relies on devices reporting their view on the signal strengths of access points, legacy mechanisms rely on access points making measurements of the signal strength of clients
For such solutions, access points may have to compare the signal strength they see on a probe request on one band with the signal strength they see for data traffic of the same station that is associated on another band
If the probe request uses a different MAC address than is used for the associated connection, then the access point will be unable to determine that the probe request is from the same device and will therefore be unable to perform the client steering action
Furthermore, APs may need to record which clients do not respond well to legacy steering attempts in order to avoid repeating the same poor experience. This requires a persistent identifier for the client device
Pre-association steering may also be impacted, depending on the specific implementation, as client devices using MAC randomisation may use one MAC address for probing and a different one for association